## Slide 1: Ex4. Flash read verification
Formal verification of a flash memory reading unit
  Show the correctness of the flash_read()
    By using randomized testing
      Randomly select the physical sectors to write four characters and set the corresponding SAMs
    By using exhaustive testing
      Create 43680 (16*15*14*13) distinct test cases
        Do not print test cases in your hardcopy to save trees
    By using CBMC
      Create environment model satisfying the invariant formula by using __CPROVER_assume() and nested loops

## Slide 2
typedef struct _SAM_type{
unsigned char offset[SECT_PER_U];
}SAM_type;
typedef struct _PU_type{
unsigned char sect[SECT_PER_U];
}PU_type;
// Environment assumption
// 0. Each unit contains 4 sectors.
// 1. There is one logical unit containing "abcd"
// 2. There are 4 physical units
// 3. The value of SAM table is 255 if the corresponding
// physical sector does not have a valid data
void flash_read(char *buf, SAM_type *SAM, PU_type *pu ){
unsigned char nSamIdx = 0;
unsigned char pu_id = 0;
unsigned char n_scts = 4; // number of sectors to read
unsigned char offset = 0; //offset of the physical sector to read
unsigned char pBuf = 0;
while(n_scts > 0){
pu_id=0;
offset = 255;
// read 1 character
while(1) {
if (SAM[pu_id].offset[nSamIdx] != 255){
offset = SAM[pu_id].offset[nSamIdx++];
buf[pBuf] = PU[pu_id].sect[offset];
break;
}
pu_id ++;
}
n_scts--;
pBuf ++;
}
}

## Slide 3
#include <stdio.h>
#include <time.h>
#include <assert.h>
#define SECT_PER_U 4
#define NUM_PHI_U 4
typedef struct _SAM_type{
unsigned char offset[SECT_PER_U];
SAM_type;
typedef struct _PU_type{
unsigned char sect[SECT_PER_U];
}PU_type;
char data[SECT_PER_U] = "abcd";
PU_type pu[NUM_PHI_U];
SAM_type SAM[NUM_PHI_U];
void randomized_test(){
unsigned int i = 0, j = 0;
unsigned char ind_pu, ind_Sect;
// Initialization
for(i = 0;i < NUM_PHI_U;i++){
for(j = 0;j < SECT_PER_U;j++){
SAM[i].offset[j] = 255;
pu[i].sect[j] = 0;
}}
while (i< SECT_PER_U) {
ind_pu = rand()%4;
ind_Sect= rand()%4;
if(pu[ind_pu].sect[ind_Sect] == 0){
pu[ind_pu].sect[ind_Sect] = data[i];
SAM[ind_pu].offset[i] = ind_Sect;
i++;
}
}
}
void main(){
char res[50];
int tc = 0;
int count = 0;
int nTC = 43680;// # of possible distribution
// 16*15*14*13
while(tc++ < nTC){
randomized_test();
flash_read(&res[count],SAM,pu);
assert(res[0] == 'a' && res[1] == 'b' &&
res[2] == 'c' && res[3] =='d');
}}
Problem #1. Random solution
ind_pu
0 1 2 3
0
1
2
3
ind_sect

## Slide 4
Problem #1. Exhaustive solution
void exhaustive_test(int *data_pos){
unsigned int i = 0, j = 0;
unsigned char ind_pu, ind_Sect;
for(i = 0;i < NUM_PHI_U;i++){
for(j = 0;j < SECT_PER_U;j++){
SAM[i].offset[j] = 255;
pu[i].sect[j] = 0;
}
}
for(i = 0;i < NUM_PHI_U;i++){
ind_pu = data_pos[i]/4;
ind_Sect = data_pos[i]%4;
pu[ind_pu].sect[ind_Sect] = data[i];
SAM[ind_pu].offset[i] = ind_Sect;
}
}
void main(){
char res[4];
int i, j,k,l, data_pos[4];
//# of all distributions = 16*15*14*13
for(i = 0;i < NUM_PHI_U * SECT_PER_U;i++){
for(j = 0;j < NUM_PHI_U * SECT_PER_U;j++){
if (j == i) continue;
for(k = 0;k < NUM_PHI_U * SECT_PER_U;k++){
if (k == i || k == j) continue;
for(l = 0;l < NUM_PHI_U * SECT_PER_U;l++){
if(l == i || l == j || l == k) continue;
data_pos[0] = i;
data_pos[1] = j;
data_pos[2] = k;
data_pos[3] = l;
exhaustive_test(data_pos);
flash_read(&res[count],SAM,pu);
assert(res[0] == 'a' && res[1] == 'b'
&& res[2] == 'c' && res[3] == 'd');
} } } } }
a |  |  | 
 | b |  | 
 |  | c | 
 |  | d | 
ind_pu
0 1 2 3
0
1
2
3
ind_sect
0 | 5 | 10 | 11
data_pos

## Slide 5
Problem #1. CBMC solution
void CBMC_environ_setting(){
unsigned int i = 0, j = 0;
unsigned char ind_pu, ind_Sect;
for(i = 0;i < NUM_PHI_U;i++){
for(j = 0;j < SECT_PER_U;j++){
SAM[i].offset[j] = 255;
pu[i].sect[j] = 0;
}}
for(i = 0;i < SECT_PER_U;i++){
ind_pu = nondet_char();
ind_Sect = nondet_char();
__CPROVER_assume(ind_pu>=0 && ind_pu <NUM_PHI_U);
__CPROVER_assume(ind_Sect>=0 && ind_Sect <SECT_PER_U);
__CPROVER_assume(pu[ind_pu].sect[ind_Sect] == 0);
pu[ind_pu].sect[ind_Sect] = data[i];
SAM[ind_pu].offset[i] = ind_Sect;
}
}
void main(){
char res[50];
int count = 0;
CBMC_environ_setting();
flash_read(&res[count],SAM,pu);
assert(res[0] == 'a' && res[1] == 'b' && res[2] == 'c' && res[3] == 'd');}
Chart: 
| Randomize | Exhaustive | CBMC
Execution time(sec) | 0.31 | 0.359 | 0.385